## Slide 1
Onkar Engine & Generator (P) Limited
Nature Of NC | Pressure plate 6 Holes Tapping Not proper |  |  |  |  |  |  | 
Issues | Tapping not Proper |  |  |  | Supplier name |  | Onkar E-14 | 
Product name | Pressure Plate | NON CONFORMITY REPORT |  |  | Lot Size/Qty. |  | 3700 Nos | 
Model | Amica & Qube | Customer | Onkar D-316 |  | NC Create Date | 29.7.2020 | NC Closure Date | 3.8.2020
Temporary Action | 100% Segregation at customer end. |  |  |  |  |  |  | 
Permanent Action | Repaired the Machine & Fixed the taping machine operator. |  |  |  |  |  |  | 
Defect Symptom | Why 1 | Why 2 |  | Why 3 | Why 4 |  | Why 5 | 
Tapping not Proper | Machine having vibration problem | Shaft Wear out |  | Machine running by unskilled operator. | Skilled operator was absent. |  | ------------ | 
Corrective Action | Machine has been repaired and segregated all defective materials by TPG gauge . |  |  |  |  |  |  | 
Preventive Action | Fixed the Machine operator and using TPG gauge in 10 pcs out of 100 pcs . Operator skill matrix prepared . |  |  |  |  |  |  | 
Prepared By:- |  |  |  |  | Approved By:- |  |  |